## Slide 1: SensorDuino
Arduino Uno & ESP8266 (NodeMCU)
By: Gerard van Seventer - 2017

## Slide 2: Functionality & Requirements
Low cost
monitor water level in two tanks via magnetic switches (3 levels)
measures:
  temperature
  barometric pressure
  air humidity
  Light
optional:
  magnetic switches (door/alarm/etc.)
  relay output (drives waterpump when level is too high)
reports directly to Domoticz by calling JSON uri

## Slide 3: Components
Arduino Nano
ESP-01 (esp8266) as Wifi shield
ESP is running NodeMCU
Logic level converter 3.3v <-> 5v
2 x 3 Switches (Water level in 2 tanks)
BMP280 barometric pressure and temperature sensor
DHT22 moisture and temperature sensor
LDR Light dependent resistor

## Slide 4: Arduino NANO Pinout

## Slide 5: ESP-01

## Slide 6: DHT22

## Slide 7: Barometric pressure & temperature
BMP280 via I2C
Newest high precision Bosch BMP280 barometric pressure & temperature sensor. Offers pressure measuring range of 300 to 1100 hPa with an accuracy of 0.01 hPa (higher accuracy than older BMP180 at 0.02 hPa resolution). Excellent for barometric pressure, elevation & vertical velocity speed measurements. It's based on piezo-resistive technology for high accuracy, ruggedness and long term stability. Comes with breadboard compatible 6-PIN header.
Includes barometric & temperature sensor
Connects to a microcontroller or Arduino via I2C bus (SCL->A5, SDA->A4) or SPI (SCL->SCK, CSB->MISO, SDA->MOSI, CSB->CS)
Two wire interface, SCL & SDA are 5V tolerant
Factory calibrated with the calibration coefficients stored in ROM
Voltage supply (VIN): 1.8V to 3.6V (3.3V typical)
Ultra low power consumption

## Slide 8: Other Sensors
LDR
Magnetic Switches
Opto isolated

## Slide 9: Logic Level Convertor 3.3V 5V

## Slide 10: Schematic

## Slide 11: Software
Arduino IDE for programming Arduino NANO
NodeMCU on ESP8266
ESPlorer
if (Serial.available()) {
digitalWrite(13, HIGH);
ESP8266.write(Serial.read());
}
function getIP()
ip = wifi.sta.getip()
print(ip)
end

## Slide 12: ESP8266 – NodeMCU API
UART is set to 9600 with no echo (uart.setup(0,9600,8,0,1,0))
Let ESP do some tasks by servicing some API’s like:
  connectAP() – Connect tot access point
  sendData() – Connect to host and send data

## Slide 13: Arduino code

## Slide 14: Flow
Power-up  Check ESP Ready  SetupESP() connectAP() wait for connect
checkSensors  sendData()
=sendData("192.168.14.100",8084,"/json.htm?type=command&param=udevice&idx=274&nvalue=0&svalue=1023")
connectAP("MySSID","AP-Password",10)
HTTP/1.1 200 OK
Content-Length: 53
Content-Type: application/json;charset=UTF-8
Cache-Control: no-cache
Pragma: no-cache
Access-Control-Allow-Origin: *
{
"status" : "OK",
"title" : "Update Device"
}
getIP() 192.168.14.19
=wifi.sta.status() 5
/json.htm?type=command&param=udevice&idx=275&nvalue=0&svalue=24.30;31.50;0

## Slide 15: ToDo
Save/load SSID & Passphrase to EEPROM
Add menu option
Enter “M” key for menu, will halt program and show menu
In Menu (shows current SSID and Passphrase(?))
  Enter “S” to enter SSID. Read keyboard string <enter> ends input
  Enter “P” to enter Pass. Read keyboard string <enter> ends input
  Enter “W” to write SSID & Passphrase to EEPROM
  Enter “Q” to quit menu and restart program (or restart Arduino?)